## Slide 1: CST8509 Part II

## Slide 2: Today's Agenda
Midterm results
Gazebo
RViz
Dynamic Programming
Monte Carlo

## Slide 3: Toolbox
Today we add Gazebo and Rviz to our RL toolbox:
  Gymnasium (Environments)
  Stable-Baselines3 (Algorithm implementations/agents)
  Gazebo (?? Simulation)
  Rviz (?? Robot Visualization)

## Slide 4: Gazebo
Gazebo is a simulator: https://gazebosim.org/home
Simulates environments
Simulates robots
Plugin-based physics, rendering, and GUI libraries
ROS integration

## Slide 5: Gazebo Versions
Gazebo versions can be confusing, because there are two choices:
  Classic Gazebo (version 11), or Gazebo11 or Gazebo-11 or Classic Gazebo
  Ignition Gazebo (version Fortress, Harmonic, etc). Note that Ignition Gazebo has been renamed to just Gazebo! This Gazebo choice can be called Gazebo, Ignition Gazebo, Gazebo Sim.
We will use Classic Gazebo 11 for Lab 4
To Install Classic Gazebo 11 on Ubuntu-desktop 22.04
  sudo apt update && sudo apt upgrade
  curl -sSL http://get.gazebosim.org | sh

## Slide 6: RL with Create3 robot
First let's imagine applying RL to our Create3 robots from CST8504
Environment:
  Image publisher
  Recording publisher (we'll ignore voice commands for now)
Agent:
  Hands Module
  Move Module
  Actions: Twist Messages from Move Module
Reward:
  Need to add a reward generator
  Need to be careful with step duration, moving target, etc

## Slide 7: Our Create 3 Setup (Last Semester)
Create 3
192.168.186.2
Loaner Laptop
Camera/Speaker/Microphone
Ubuntu 22.04/ROS2 Humble
Wired:192.168.186.3
WIFI: from your router
Your Laptop
WIFI: from your router
Robot of ROS 2 Nodes
Nodes on network communicate
Thinking Part
Wheels/Moving Part

## Slide 8: Our Create 3 Setup (Simulated)
Loaner Laptop
Camera/Speaker/Microphone
Ubuntu 22.04/ROS2 Humble
Robot of ROS 2 Nodes
Gazebo Nodes are on Laptop
Nodes on Laptop communicate
Thinking Part
Wheels/Moving Part
Create 3
Gazebo
This still uses the Laptop Camera (remember we made the turtlesim move with our actual hand in front of the laptop camera)
Lab4 involves adding a Virtual Gazebo Camera that sees the Gazebo world

## Slide 9: Why is Gazebo so important for our RL?
Assuming we work out the details RL with the Create3, how will we train the agent?
Q: Who is going to move their hand around during training?
  What if training takes 3 days, won't that person get tired?
Q: How do we maintain robot safety in early training stages?
  During training, the robot tries a dangerous action?
A: If the hand person and the robot are simulated, they can't get tired or hurt
  Gazebo can simulate the robot, the person/hand, and the environment

## Slide 10: RL Diagrams so far
Agent:
Q-Learning or
Stable-baselines3:
DQN or PPO or…
Gymnasium Environment
Prolog model
Swiplserver
Rt+1
St+1
Rt
St
action At
render()
PyGame

## Slide 11: Where do ROS 2 and Gazebo fit into this picture?
The Robot Operating System (ROS 1 and ROS 2) is a set of software libraries and tools for building robot applications.
Gazebo supports ROS integration
  Gazebo version of Create3 publishes on ROS 2 topics

## Slide 12: RL Diagrams with virtual Create 3
Agent:
Q-Learning or
Stable-baselines3:
DQN or PPO or…
Gymnasium Environment
Rt+1
St+1
Rt
St
action At
G
Create 3
Gazebo
Loaner Laptop
ROS 2 Nodes Communicating

## Slide 13: iRobot Create 3 Simulator
iRobot has already done the work of creating the Gazebo simulated Create 3
AWS has already done the work of creating the Gazebo AWS small house world
iRobot Create 3 Simulator:
https://iroboteducation.github.io/create3_docs/sim/setup/
Instructions for installing and running (we use Classic Gazebo 11):
  https://github.com/iRobotEducation/create3_sim

## Slide 14: Adding a Camera to Create3
Unified Robotic Description Format (URDF)
File format used in ROS
File format used for Create 3 simulator
Build process will convert this to SDF
Simulation Description Format (SDF)
New format created for use in Gazebo
Intended to address shortcomings of URDF
Xacro
XML macro language (both URDF and SDF are XML)

## Slide 15: URDF Details
We won't be digging deeper than just adding our camera in Lab 4, but for those who want to dig deeper:
https://docs.ros.org/en/iron/Tutorials/Intermediate/URDF/Building-a-Visual-Robot-Model-with-URDF-from-Scratch.html

## Slide 16: Rviz
Graphical interface for viewing robot, sensor data, maps, and more.
https://turtlebot.github.io/turtlebot4-user-manual/software/rviz.html

## Slide 17: Dynamic Programming
DP is a collection of algorithms to compute optimal policies given a perfect model
Policy Evaluation: compute the state-value function v for an arbitrary policy
  Iteratively follow the policy, use Bellman Equation to update value function (keep doing this until differences from previous are "small")
Policy Improvement: make it greedy with respect to the new value function
Policy Iteration: iterate policy evaluation and improvement
  drawback is that each of its iterations involves policy evaluation
Value Iteration: like Policy Iteration but…
  Difference is that Policy Evaluation is stopped after one iteration

## Slide 18: Dynamic Programming
Jupyter Notebook implements iterative value iteration:
dynamic.ipynb

## Slide 19: Monte Carlo
Dynamic Programming required knowing the model in advance (results of actions)
Monte Carlo methods are based on averaging sample returns
Complete an episode and afterwards, record the returns such that returns are averaged over time
All episodes must terminate
State looping: distinguish between visits to the same state in a single episode:
first-visit methods
every-visit methods

## Slide 20: MC methods
How to ensure every action is tried:
Exploring starts: try a random state/action pair at the beginning of each episode
  Can't be used with an environment
Consider only policies that are stochastic with a nonzero probability of selecting all actions in each state
epsilon-soft policies: every action has a chance
epsilon-greedy: example of epsilon-soft policy

## Slide 21: Monte Carlo
The agent goes to the end of an episode without changing the Q-table
After an episode ends, the agent backs up and updates the q-table (just until the first change)
monte_carlo.ipynb implements algorithm on Page 111 of Sutton + Barto textbook